TITLE:  CLIPBOARD

DIMENSIONS:  1\2” x 9” x 121\2”

TOOLS AND EQUIPMENT:	Jointer	Surface Planer

Table Saw	Shaper

Vibrating Sander	Radial Arm Saw

Drill	Portable Belt Sander

PROCEDURE:

- Secure strips of Hardwood, making sure they are 5\8” thick, and at least 13” in length.

- Dry clamp the strips to make sure your joints are tight.  Check to see if you have at least 10” in width.

- Loosen the clamps and apply glue, then re-clamp.

- Remove bar clamps, clean and put them back on the clamp rack.

- Clamp your stock to the workbench and scrape the excess glue off with a cabinet scraper.  Remove the dried glue from both sides.

- Surface both sides’ smooth, finished thickness should be 1\2”.  Set the planer to 9\16” and run on side of the clipboard.  Adjust the planer setting to 1\2” and surface the other side.

- Joint the best edge on the jointer. (Remember you only joint one edge).

- Cut your stock to 9” in width on the table saw.  The edge you jointed goes next to the fence when you run your wood through the table saw.

- Cut to length on the radial arm saw.  First square one edge and then flip the stock over and measure 12 3\4” then cut the clipboard to exact length.

- Set up the shaper with a 1\4” rounding over bit. Round the end grain on both ends and then the both edges.

- Sand the clipboard with #80 #100 #150 grits sandpaper.  Note:  You may need to use the portable belt sander to remove surface planer marks, if so use the portable belt sander first and then #80 #100 #150.

- Apply Danish Oil to your project.  The first day apply a coat of oil to your project and wait 10 minutes.  Apply a second coat of oil and wait 10 minutes and then buff off the excess oil with a cotton rag.  The second day apply a coat of oil on your project, wait 10 minutes and the buff off the excess with a cotton rag.  The third day repeat what you did on the second day.

- Apply a thin coat of paste wax to your project and the remove the wax with 00 steel wool.  Again put a thin coat of paste wax on your project and let it sit for 10 minutes and the buff off the excess wax with a cotton rag.

- Attaching Clip: Chuck a 3/32” drill bit into a drill.  Acquire 2- 3\8x #8 pan head screws and a clip from the instructor.  Find the center of the clipboard and align the center of the clip on this mark and drill a 3\32” hole into the board, about 1\8” deep.  Screw in one pan head screw.  Drill the other hole and screw in the other screw.