TITLE: END TABLE          					MATERIALS:

4- 3\4” X 3” X 19”

4- 3\4” X 2 1\4” X 19”

1- 3\4” X 24” X 24”

4- 3\4’ X 3” X 22”

4- 3\4” X 1 1\2” X 16”

DIMENSIONS: 24” SQUARE AND 20” TALL

MATERIAL AMOUNT:  9.3 bd. ft.

# TOOLS AND EQUIPMENT:  	SURFACE PLANER  		RADIAL ARM SAW

JOINTER		TABLE SAW

SHAPER		BELT SANDER

BISCUIT MACHINE		HAND DRILLS

DRILL PRESS

PROCEDURE:

- Determine the type of wood that you want to use in the construction of your End Table.

- Start with the legs.  Acquire a board from the lumber rack that is at least 5 1\2” to 6” in width.  If there isn’t the correct width talk to your instructor.

- Rough cut four pieces of wood to 20” in length on the radial arm saw.  Remember to keep your hands a least 4” away from the blade and to pull out slowly.

- Surface the four boards to 3\4” in thickness.  Measure the thickness of the wood and set the planer to 1\16” less than the actual thickness of your wood.  Run the boards through the planer.  Repeat this process until you reach the correct thickness.(3\4”)

- Joint one edge of each board.  Make sure the jointer is set at the correct depth of cut, 1\8”.

- Using the table saw rip a 3” and a 2 1\4” piece form each board.  Remember that the jointed edge of your board goes next to the fence of the table saw.

- The next step is to use the biscuit machine.  Ask the instructor for help in completing this process.

- After you have cut the slots for the biscuits sand the insides of your legs with the belt sander.

- Glue the boards together to form your legs.  Use the parallel clamps for this operation.

- Be sure to clean up any glue on the inside of the legs with a damp rag.

- Scrape off the excess glue from the boards with a glue scraper.  Use a bench vice to secure your wood to the workbench while you scrape off the glue.

- Sand the outside surfaces of your legs on the belt sander.

- Square one end of each leg on the radial arm saw.  Set up the STOP BLOCK on the radial arm saw to 19 1\4” from the blade.  Place the squared end of your leg next to the stop block and cut to length, repeat this procedure to each leg.

- Set up the shaper with a 3\8” rounding over bit.  With the exception of one end, route all outside edges.  Remember to run your wood from right to left.

- Sand all outside surfaces, of your legs, with #80-#100-#150 grits sandpaper.

- The next step is to make the top of your end table.  Find a board that is a little over 6” in width.

- Rough cut four pieces to 25” in length on the radial arm saw.

- Surface plane the boards to 3\4” in thickness.

- Lay out your boards on the workbench and determine in what order they will be placed.  As you are doing this look for the most interesting grain patterns and color.

- Joint all inside edges on the boards.

- Use the biscuit machine and cut the slots in your boards.

- Dry clamp the top and look at all edges to make sure that there aren’t any gaps.

- Loosen the clamps and apply glue to the edges and re-clamp.

- Remove the clamps, clean and replace them on the clamp rack.

- Secure your top to the bench and scrape off the excess glue.

- Joint one edge of the top with the jointer.

- With the jointed edge next to the fence of the table saw rip to the width of 24”.

- Square one end on the radial arm saw.  The radial arm saw will only cut to 16”.  So cut part way through and then flip the top over and finish the cut.

- Keeping the squared end next to the fence on the table saw cut the top to 24” in length.

- Secure the top to the workbench and sand both top and bottom with the portable belt sander.

- Route the top edges of the tabletop with a 1\2” rounding over bit.  Use the portable router for this operation.

- Sand all surfaces of the top with #80-#100-#150 grits sandpaper.

- The next step is to make the aprons.  Find a board that is a little over 6 1\2” in width and cut two pieces to 23” in length on the radial arm saw.

- Surface plane to 3\4” in thickness.

- Joint one edge on the jointer.

- Rip two pieces from each board to 3” in width.

- Set up the shaper with a 3\8” rounding over bit.  Round over one edge, top and bottom, on each of the four aprons.

- Sand the aprons with #80-#100-#150 grits sandpaper.

- Find some scrap wood that you can use to make 4-3\4” x 1 13/8” x 16”pieces of wood.  These will be used in attaching your aprons to the tabletop.

- Cut to width on the table saw and then cut to length on the radial arm saw.

- Drill four 1\8” holes all the way through the thickness and all way through the width of your wood.  These holes should be evenly spaced out along your wood.  Starting about 1” from the edge.

- Sand the four pieces on the belt sander.

- Counter sink all of the holes with a 3\8” forstner bit.  First determine the length of the screws that you will use.  For the 3\4” dimension use a 1 1\4” screw.  Counter sink the hole 1|8” so that 5\8” of the screw is sticking out of the wood.  For the 1 13/8” dimension use a 2” screw and the counter sink is 1\8” in depth.

- Set your end table top on the workbench and then position the four legs.  They should be inset about 1” from the edges.

- Measure the distance from inside to inside between the legs.  This should be the same from each leg if they are positioned correctly.

- Cut two aprons to this length and position them between the legs and measure between the two aprons.  Cut the other two aprons to this length.  They should be 1 1\2” shorter than the first two aprons.

- Attach the four strips that you drilled and countered bored to the aprons.  Lay the apron on its side and center one of the strips to the bottom edge of the apron.  Make sure the counter bore is facing up and that the two edges are flush.  Drill through the existing holes of the strip into the apron using a 1\8” drill bit.  Only go part way through the apron.  Attach the strip to the apron with the portable screw gun and 1 1\4” screws.  Continue the process with the other three aprons.

- Place the tabletop; face down, on top of your workbench.  Place the four legs in the correct position and place the aprons between the legs.  Attach the aprons to the tabletop by drilling 1\8” holes into the tabletop through the existing holes.  Be careful to only drill part way through the tabletop.  Secure the aprons to the tabletop with the portable screw gun and the 2” screws.

- Attach the legs to the aprons.  Spread a small amount of glue on the leg where it comes in contact with the apron.  Hold in position and drill a 1\8” hole through the apron and into the leg.  Use a portable screw gun and screw it in place.  You’ll need to put four screws in each leg.

- After all four legs are attached measure between the legs near the top and make sure the measurement is the same at the end of the legs.  If it isn’t cut spacers to the correct length and put them between your legs.  Allow the glue to setup over night.

- Do any finish sanding that is required before you apply Danish Oil.

- Apply Danish Oil to your end table and let it soak in for about 10 min. and then apply a second coat and let it soak in about 15 min.  Remove any excess oil with a cotton rag.  The next day apply a coat of oil and let it soak in for 10 min. and then buff off the excess with a cotton rag.  Repeat this process on the third day.

- The End Table needs to be waxed to give it along lasting finish.  Apply a thin coat of paste wax over all surfaces of the end table.  Remove the wax with 00 steel wool; rub vigorously with the grain.  Apply a second coat of wax and allow it to sit for about 10 min. and the buff off the excess wax with a cotton rag.

THAT’S IT!!!!  GREAT JOB ON A BEAUTIFUL END TABLE!!!!!!