Jointer Safety Information Sheet

True / False Test

- Always make sure the guard is in place and operating properly before using the jointer. ___

- Always wear eye protection when using the jointer.___

- Always inspect wood for embedded foreign objects like nails and staples before running it through the jointer. ___

- Always keep your infeed and outfeed tables clear of temporary storage.___

- Never release the work until you have pushed it all the way clear of the blade.___

- Never cut end grain unless you have checked with the instructor first.___

- When cutting small pieces that place your hands within 4” of the blade, use a push stick.___

- Never face cut material that is less than 3/8” thick.___

- When cutting, keep even pressure on the front and rear of the board.___

- Never place your fingers or hand in the path of the blade.___

- Always hold your work firmly against the fence.

- Avoid awkward operations and hand positions.___

- Always unplug the saw before working on or changing the blade.___

- Always report any problems with the jointer to your supervisor.___

I have read and understand the above safety rules regarding the circular saw.  I have also been given hands on instruction by my instructor.

Sign your name___________________________________ Date______________

Print your name___________________________________