Table Saw Safety

True / False Test

- Always make sure the guard is in place and operating properly before using the table saw, except when:

- using a sled for crosscutting___

- making a cut with the blade tilted___

- using a miter gauge___

- using jigs and fixtures that would conflict with the blade guard___

- you have your instructor’s permission___

- Always inspect the blade before operating the table saw.  Make sure:

- the blade is the proper one for the task at hand. ___

- the blade is set no more than ¼ inch above the wood before cutting. ___

- that the blade is installed properly___

- Always wear eye protection when using a table saw.___

- Always inspect wood for embedded foreign objects like nails and staples before running it through the table saw.__

- Never stand in line with the blade. ___

- Always be aware that material can kick back if the wood you are cutting binds between the blade and the rip fence or other fixed objects.___

- Always keep your work area clean.___

- Never release the work until you have pushed it all the way clear of the blade.___

- Never leave material between the fence and the blade while the blade is turning.___

- When cutting small pieces (less than 4” wide), use a push stick.___

- Always get instructor permission before making a narrow rip, which is a rip that is unsafe to make with the blade guard in place.  When making a narrow rip, raise the guard and crank it horizontally out of your way.___

- When cutting, push the work between the blade and the fence only, not the side away from the blade and fence.___

- Never use the fence and miter gauge at the same time while making a cut.___

- Never place your fingers or hand in the path of the blade.___

- Never operate the table saw free hand.___

- Never reach over a saw blade to remove scraps.___

- Avoid awkward operations and hand positions.___

- Always unplug the saw before working on or changing the blade.___

- Always report any problems with the table saw to your supervisor.___

I have read and understand the above safety rules regarding the table saw.  I have also been given hands on instruction by my instructor.

Sign your name___________________________________ Date______________

Print your name___________________________________